## Slide 1
SafeDrones: Real-Time Reliability Evaluation of UAVs using Executable Digital Dependable Identities
k.aslansefat@hull.ac.uk
Koorosh Aslansefat, Panagiota Nikolaou, Martin Walker, Mohammed Naveed Akram, Ioannis Sorokos, Jan Reich, Panayiotis Kolios, Maria K. Michael, Theocharis Theocharides, Georgios Ellinas, Daniel Schneider and Yiannis Papadopoulos

## Slide 2
Table of Content
Secure and Safe Multi-Robot Systems
Funding: H2020-ICT-2020-2
Duration: 3 Years, Starting from January 1st, 2021
17 Partners
~ 7M € Budget
Coordination by The Open Group Limited

## Slide 3
Table of Content
What we are going to discuss
Introduction
Brief introduction for drones and the importance of reliability evaluation
SafeDrones, Markov Modelling
SafeDrones Goals, Markov modelling of drones with different configurations, simplification of models
Numerical Results
Numerical results for reliability and MTTF
Conclusion
A conclusion and suggestions for future works

## Slide 4
Applications of Drones
Cargo Delivery
Entertainment
Agricultural
Search and Rescue
UAV Applications
[3]

## Slide 5
Drones Market
A quick report
Reference: www.droneii.com

## Slide 6
UAV-like eVTOLs
Reference: www.evtol.com
EHANG 216
Airbus Air Taxi

## Slide 7
Background

## Slide 8
A Simple Structure of Hidden Markov Model
OP
D1
D2
F
D3
O1
O2
O3
O4
O5
On
System’s
Observations
Hidden States
of System’s
Operation

## Slide 9
A
B
TOP
Merging the Idea of Hidden Markov Model with DFT
Abnormal
Temperature
Abnormal
Vibration
Abnormal
Displacement
Abnormal
Condition n
Observations
Hidden Model
© K. Aslansefat, 2018

## Slide 10
Sliding Window-based Diagnostic and Prognostic
W1
W2
W3
Wn
n operating points
Sliding Window #1
L
Window Length
l
Window Overlaps

## Slide 11
A
B
TOP
A Basic Event in DFT and Phased Type Markov Model
A
F
A
B
B
F
Trivedi, K., & Bobbio, A. (2017). Phase-Type Expansion. In Reliability and Availability Engineering: Modelling, Analysis, and Applications (pp. 551-574). Cambridge: Cambridge University Press. doi:10.1017/9781316163047.020
N = 2
OP
D1
F
OP
D1
F
D2
OP
D1
D2
F
D3
N = 3
N = 4
Convert the model to a Acyclic Phased-Type Markov model

## Slide 12
Sliding Window-based Diagnostic and Prognostic
OP
D1
D2
F
D3
OP
D1
D2
F
D3
OP
D1
D2
F
D3
OP
D1
D2
F
D3
OP
D1
D2
F
D3
Calculating the Probability to Failure and also Mean Time To Failure (MTTF)
A
B
TOP

## Slide 14
SafeDrones Project Goal
Providing safety and reliability models for different parts of Drones.
Reliability and Safety Modelling
Online safety and reliability monitoring of Drones.
Safety and Reliability Monitoring
EDDI: Executable Digital Dependable Identifier
Providing EDDI functions to be executed on robot embedded system.
© K. Aslansefat, 2021
https://github.com/koo-ec/SafeDrones

## Slide 16
Propulsion System

## Slide 17
Markov Modelling
Hexa-Copter PNPNPN Configuration
Aslansefat, K., Marques, F., Mendonça, R., & Barata, J. (2019, May). A Markov process-based approach for reliability evaluation of the propulsion system in multi-rotor drones. In Doctoral Conference on Computing, Electrical and Industrial Systems (pp. 91-98). Springer.

## Slide 18
Simplified Markov Model
Hexa-Copter PNPNPN Configuration
Aslansefat, K., Marques, F., Mendonça, R., & Barata, J. (2019, May). A Markov process-based approach for reliability evaluation of the propulsion system in multi-rotor drones. In Doctoral Conference on Computing, Electrical and Industrial Systems (pp. 91-98). Springer.

## Slide 19
Markov Modelling
Hexa-Copter PPNNPN Configuration
Aslansefat, K., Marques, F., Mendonça, R., & Barata, J. (2019, May). A Markov process-based approach for reliability evaluation of the propulsion system in multi-rotor drones. In Doctoral Conference on Computing, Electrical and Industrial Systems (pp. 91-98). Springer.

## Slide 20
Simplified Markov Model
Hexa-Copter PPNNPN Configuration
Aslansefat, K., Marques, F., Mendonça, R., & Barata, J. (2019, May). A Markov process-based approach for reliability evaluation of the propulsion system in multi-rotor drones. In Doctoral Conference on Computing, Electrical and Industrial Systems (pp. 91-98). Springer.

## Slide 21
6
M
5
M
4
M
4*
M
3
M
F
© K. Aslansefat, 2021

## Slide 22
6
M
5
M
4
M
4*
M
3
M
F
© K. Aslansefat, 2021

## Slide 23
6
M
5
M
4
M
4*
M
3
M
F
© K. Aslansefat, 2021

## Slide 24
6
M
5
M
4
M
4*
M
3
M
F
© K. Aslansefat, 2021

## Slide 25
6
M
5
M
4
M
4*
M
3
M
F
M_S
PNPNPN Configuration

## Slide 26
6
M
5
M
4
M
4*
M
3
M
F
M_S
PNPNPN Configuration

## Slide 27
27
Battery System

## Slide 28
Kabir, S., Aslansefat, K., Sorokos, I., Papadopoulos, Y., & Gheraibia, Y. (2019, October). A conceptual framework to incorporate complex basic events in HiP-HOPS. In International Symposium on Model-Based Safety and Assessment (pp. 109-124). Springer.
Battery System Degradation and Failure

## Slide 30
Arrhenius Equation
(Ottavi, M. et al., 2014)

## Slide 33
Application of SafeDrones for Multi-robot Precision Agriculture
© K. Aslansefat, 2022
Consider a scenario in which three UAVs are tasked to scan three fields in parallel when an internal fault occurs in UAV #3. Although it does not cause immediate failure, SafeDrones re-evaluates the reliability at runtime and determines it increases the risk above a dangerous threshold, so in order to reduce the risk of collision or spraying out of bounds, UAV #3 activates a fail-safe mechanism and returns to base. If UAV #2 has required availability, its mission can then be updated to cover the third field.

## Slide 34
Safe Distance
Unsafe Distance
Application of SafeDrones for Offshore Wind Turbine Blade Inspection
e.g. - Motor Failure:
Updating the Reliability Profile and Required Safe Distance
© K. Aslansefat, 2022
Considering the widely variable wind speeds encountered, a fault in the UAV that reduces controllability risks collision with a blade, causing damage to both UAV and wind turbine. The SafeDrones approach allows us to assess risk in real-time in response to the occurrence of faults by providing a runtime evaluation of reliability. Using this information, the drone can adapt its behaviour accordingly, e.g. by increasing safe distance to reduce risk of collision.

## Slide 37
© KIOS 2022

## Slide 38
Conclusion
To help address the problems of UAV reliability and risk assessment, particularly at runtime where operational and environmental factors are hard to predict, the SafeDrones reliability modelling approach has been proposed.
It employs a combination of FTA with CBEs to support real-time reliability evaluation as a prototype of the EDDI concept.
It introduces a novel symptoms layer in Fault Tree Analysis to integrate it with runtime monitoring data.
To illustrate SafeDrones, we applied it to a power network inspection use case to show how real-time reliability evaluation can be used to anticipate imminent failures and prevent accidents by recommending appropriate responses.

## Slide 39
SafeDrones
ConSerts
Updating Reliability Profile
Final Decisions
e.g., Aborting mission and
Emergency Landing
Providing Safety Guarantees
Environment Information
e.g., Wind Speed and Direction
DDI
Future Works

## Slide 40
References
[1] Trivedi, K., & Bobbio, A. (2017). Phase-Type Expansion. In Reliability and Availability Engineering: Modelling, Analysis, and Applications (pp. 551-574). Cambridge: Cambridge University Press.
[2] Aslansefat, K., Marques, F., Mendonça, R., & Barata, J. (2019, May). A markov process-based approach for reliability evaluation of the propulsion system in multi-rotor drones. In Doctoral Conference on Computing, Electrical and Industrial Systems (pp. 91-98). Springer.
[3] Kabir, S., Aslansefat, K., Sorokos, I., Papadopoulos, Y., & Gheraibia, Y. (2019, October). A conceptual framework to incorporate complex basic events in HiP-HOPS. In International Symposium on Model-Based Safety and Assessment (pp. 109-124). Springer.
[4] Ottavi, M., Pontarelli, S., Gizopoulos, D., Bolchini, C., Michael, M.K., Anghel, L., Tahoori, M., Paschalis, A., Reviriego, P., Bringmann, O., et al.: Dependable multicore architectures at nanoscale: The view from europe. IEEE Design & Test, 32(2), 17–28 (2014).
[5] Armengaud, E., Schneider, D., Reich, J., Sorokos, I., Papadopoulos, Y., Zeller, M., ... & Kabir, S. (2021, February). DDI: A novel technology and innovation model for dependable, collaborative and autonomous systems. In 2021 Design, Automation & Test in Europe Conference & Exhibition (DATE) (pp. 1626-1631).

## Slide 41
Thanks for Your Attention
If you have any question, please feel free to ask

## Slide 44
GPS Failure

## Slide 46
100
110
120
130
140
150
160
170
180
190
200
Time
0.72
0.74
0.76
0.78
0.8
0.82
0.84
0.86
0.88
0.9
P
r
o
b
a
b
i
l
i
t
y
o
f
F
a
i
l
u
r
e
No Failure
One Motor Failure without Uncertainty
One Motor Failure with 30% Uncertainty
One Motor Failure with 50% Uncertainty